## Slide 1: Storyboard – Dangerous Goods Acceptance
CXA

## Slide 2: Objective
The objective of the game will be to swiftly and accurately identify if DG shipment can be accepted or not.
The Player will need to identify every reason if the shipment needs to be rejected based on the documents (AWB and DGD) and package the Player receives.

## Slide 3: Game Structure / Background
The game will have 3 locations to recreate acceptance counter, warehouse, and waiting area for truck drivers.

## Slide 4: DashBoard
The overlay will have various display. Some examples can be:
  DGR 4.2 Button (to popup the 4.2 information)
  AWB Button (to popup AWB document)
  DGD Button (to popup DGD document)
  Package Button (to show the package)
  Hint Button (to popup any hint on where the shipment might have issue)
  Timer (to show how long it took for player to complete the game)
  Scoreboard (to show real-time scoring)
  Truck Driver Queue (to show how many truck drivers are waiting)

## Slide 5: Gameplay
There will be 2 different play modes within the game.
  Standard mode
    Beginner level
    Intermediate level
    Advance level
  Time Trial Mode

## Slide 6: Standard Mode: Overall
The player will be given total of 5 shipments (2 correct & 3 incorrect) to check and determine whether the shipment can be accepted or rejected.
There will be Truck drivers entering the queue at a 1.5 mins interval.
If the player determines that the shipment needs to be rejected, the player must identify all the errors.
The score will be given based on the speed and the accuracy of the error identified during set amount of shipment.

## Slide 7: Standard Mode: Beginner Level
The player will need to verify and check 5 shipments to complete the game.
The shipments will consist of 2 correct shipments and 3 incorrect shipments
The incorrect shipments will have 1~2 errors within AWB, DGD, and package.
The type of shipment the player will receive are the following
  Excepted Quantity (REQ)
  Dry Ice with non-DG
  Non-Radioactive DG

## Slide 8: Standard Mode: Intermediate level
The player will need to verify and check 5 shipments to complete the game.
The shipments will consist of 2 correct shipments and 3 incorrect shipments
The incorrect shipments will have 2~3 errors within AWB, DGD, and package.
The type of shipment the player will receive are the following
  All type from previous level
  Excepted Lithium Batteries
  Limited Quantity

## Slide 9: Standard Mode: Advance Level
The player will need to verify and check 5 shipments to complete the game.
The shipments will consist of 2 correct shipments and 3 incorrect shipments
The incorrect shipments will have 3~4 errors within AWB, DGD, and package.
The type of shipment the player will receive are the following
  All type from previous levels
  Radioactive DG
  Lithium Batteries (UN3480 Section 1A & 1B)

## Slide 10: Time Trial Mode
The player will be given a set time duration (e.g. 5mins) to correctly accept and reject shipments much as the player can.
The shipments will be randomly given from the Standard Mode and some only from Time Trial Mode.
The score will be given based on the amount and the accuracy of the error identified during the set time duration.

## Slide 11: Elements Provided by Shipper In the Acceptance Check
Dangerous Goods cargo(es)
Completed Shipper’s Declaration for Dangerous Goods (DGD)
Completed Air Waybill (AWB)

## Slide 12: Types of DG Shipments

## Slide 13: Types of DG Shipments
Excepted Quantity
(REQ)
Or
Dry Ice Packed with non DG
Non-Radioactive Shipment
Radioactive Shipment
Excepted
Lithium Battery

## Slide 14: Excepted Quantity (REQ)

## Slide 15: Excepted Quantity
Shipment Information
UN Number | UN 2215
Proper Shipping Name | Maleic anhydride
Class | 8
Packing Group | III
EQ Code | E1
Max Net Quantity Per Outer Packaging | 1kg / 1L
Actual Net Quantity in Outer Packaging | 0.8kg

## Slide 16: Excepted Quantity
Correct Package
SHIPPER
ABC Chemicals
1 Chun Wan Road
Chek Lap Kok
Hong Kong
Front:
Left:
Right:
CATHAY PACIFIC
AWB No.
160 8800 8782
Destination Total No. of Pcs
SIN 1
Fast Cargo HK Ltd.
HAWB No. Origin
HKG-1234 HKG
Destination HAWB Pieces
SIN 1
CONSIGNEE
XYZ Pty LTD
3 Airport Road
Singapore
8

## Slide 17: Excepted Quantity
Incorrect Package
SHIPPER
ABC Chemicals
1 Chun Wan Road
Chek Lap Kok
Hong Kong
Front:
Left:
Right:
CATHAY PACIFIC
AWB No.
160 8800 8782
Destination Total No. of Pcs
SIN 1
Fast Cargo HK Ltd.
HAWB No. Origin
HKG-1234 HKG
Destination HAWB Pieces
SIN 1
CONSIGNEE
XYZ Pty LTD
3 Airport Road
Singapore
8

## Slide 18: Excepted Quantity
Correct Air Waybill
Maleic anhydride
UN 2215
Dangerous Goods in Excepted Quantities
1 1.5 K

## Slide 19: Excepted Quantity
Incorrect Air Waybill
Maleic anhydride
Dangerous Goods in Excepted Quantities
1 1.5 K

## Slide 20: Dry Ice Packed With Non-DG

## Slide 21: Dry Ice Packed with Non-DG
Shipment Information
UN Number |  | UN 1845
Proper Shipping Name |  | Dry ice Carbon dioxide, solid
Class |  | 9
Packing Group |  | /
Passenger & Cargo Aircraft | Packing Instruction | 954
 | Max Net Quantity Per Package | 200 kg
Cargo Aircraft Only | Packing Instruction | 954
 | Max Net Quantity Per Package | 200 kg
Actual Net Quantity in Package | 2 kg

## Slide 22: Dry Ice Packed with Non-DG
Correct Package
SHIPPER
ABC Chemicals
1 Chun Wan Road
Chek Lap Kok
Hong Kong
Front:
Left:
Right:
CATHAY PACIFIC
AWB No.
160 8800 8782
Destination Total No. of Pcs
SIN 1
Fast Cargo HK Ltd.
HAWB No. Origin
HKG-1234 HKG
Destination HAWB Pieces
SIN 1
CONSIGNEE
XYZ Pty LTD
3 Airport Road
Singapore
UN 1845
Dry Ice
Net Quantity 2kg

## Slide 23: Dry Ice Packed with Non-DG
Incorrect Package
SHIPPER
ABC Chemicals
1 Chun Wan Road
Chek Lap Kok
Hong Kong
Front:
Left:
Right:
CATHAY PACIFIC
AWB No.
160 8800 8782
Destination Total No. of Pcs
SIN 1
Fast Cargo HK Ltd.
HAWB No. Origin
HKG-1234 HKG
Destination HAWB Pieces
SIN 1
CONSIGNEE
XYZ Pty LTD
3 Airport Road
Singapore
UN 1845
Dry Ice

## Slide 24: Dry Ice Packed with Non-DG
Correct Air Waybill
Frozen Meat
UN 1845
Dry ice
1 x 2 kg
2 12.0 K
Note: 2 packages under this Air Waybill, but only 1 package contains dry ice

## Slide 25: Dry Ice Packed with Non-DG
Incorrect Air Waybill
Frozen Meat
UN 1845
Dry ice
2 12.0 K
Note: 2 packages under this Air Waybill, but only 1 package contains dry ice

## Slide 26: Excepted Lithium Ion Battery (UN 3481)

## Slide 27: Excepted Lithium Ion Battery (UN 3481)
Shipment Information
UN Number |  | UN 3481
Proper Shipping Name |  | Lithium Ion Batteries Packed with Equipment
Class |  | 9
Packing Group |  | /
Packing Instruction |  | 966 – Section II
Passenger aircraft | Net Quantity of Lithium Ion Cells or Batteries Per Package | 5 kg
Cargo aircraft | Net Quantity of Lithium Ion Cells or Batteries Per Package | 5 kg
Actual Net Quantity of Lithium Ion Batteries in Package | 3 kg
Note: 2 PSNs for 1 UN number. Must provide actual shipment info to avoid confusion

## Slide 28: Excepted Lithium Ion Battery (UN 3481)
Correct Package
SHIPPER
ABC Chemicals
1 Chun Wan Road
Chek Lap Kok
Hong Kong
Front:
Left:
Right:
CATHAY PACIFIC
AWB No.
160 8800 8782
Destination Total No. of Pcs
SIN 1
Fast Cargo HK Ltd.
HAWB No. Origin
HKG-1234 HKG
Destination HAWB Pieces
SIN 1
CONSIGNEE
XYZ Pty LTD
3 Airport Road
Singapore
UN3481

## Slide 29: Excepted Lithium Ion Battery (UN 3481)
Incorrect Package
SHIPPER
ABC Chemicals
1 Chun Wan Road
Chek Lap Kok
Hong Kong
Front:
Left:
Right:
CATHAY PACIFIC
AWB No.
160 8800 8782
Destination Total No. of Pcs
SIN 1
Fast Cargo HK Ltd.
HAWB No. Origin
HKG-1234 HKG
Destination HAWB Pieces
SIN 1
CONSIGNEE
XYZ Pty LTD
3 Airport Road
Singapore

## Slide 30: Excepted Lithium Ion Battery (UN 3481)
Correct Air Waybill
Lithium ion batteries in compliance with Section II of PI 966

## Slide 31: Excepted Lithium Ion Battery (UN 3481)
Incorrect Air Waybill
Lithium ion batteries packed with equipment in compliance with Section II of PI 966

## Slide 32: Excepted Lithium Battery (UN 3091)

## Slide 33: Excepted Lithium Battery (UN 3091)
Shipment Information
UN Number |  | UN 3091
Proper Shipping Name |  | Lithium Metal Batteries Packed with Equipment
Class |  | 9
Packing Group |  | /
Packing Instruction |  | 969 – Section II
Passenger aircraft | Net Quantity of Lithium Metal Cells or Batteries Per Package | 5 kg
Cargo aircraft | Net Quantity of Lithium Metal Cells or Batteries Per Package | 5 kg
Actual Net Quantity of Lithium Metal Batteries in Package | 1.5 kg
Note: 2 PSNs for 1 UN number. Must provide actual shipment info to avoid confusion

## Slide 34: Excepted Lithium Battery (UN 3091)
Correct Package
SHIPPER
ABC Chemicals
1 Chun Wan Road
Chek Lap Kok
Hong Kong
Front:
Left:
Right:
CATHAY PACIFIC
AWB No.
160 8800 8782
Destination Total No. of Pcs
SIN 1
Fast Cargo HK Ltd.
HAWB No. Origin
HKG-1234 HKG
Destination HAWB Pieces
SIN 1
CONSIGNEE
XYZ Pty LTD
3 Airport Road
Singapore
UN3091

## Slide 35: Excepted Lithium Battery (UN 3091)
Incorrect Package
SHIPPER
ABC Chemicals
1 Chun Wan Road
Chek Lap Kok
Hong Kong
Front:
Left:
Right:
CATHAY PACIFIC
AWB No.
160 8800 8782
Destination Total No. of Pcs
SIN 1
Fast Cargo HK Ltd.
HAWB No. Origin
HKG-1234 HKG
Destination HAWB Pieces
SIN 1
CONSIGNEE
XYZ Pty LTD
3 Airport Road
Singapore
UN3091

## Slide 36: Excepted Lithium Battery (UN 3091)
Correct Air Waybill
Lithium metal batteries in compliance with Section II of PI 969

## Slide 37: Excepted Lithium Battery (UN 3091)
Incorrect Air Waybill
Lithium metal batteries in compliance with PI 969

## Slide 38: Non-Radioactive Dangerous Good

## Slide 39: Non Radioactive
Shipment Information
UN Number |  |  | UN 2841
Proper Shipping Name |  |  | Di-n-amylamine
Class |  |  | 3 (6.1)
Packing Group |  |  | III
Passenger & Cargo Aircraft | Ltd Qty | Packing Instruction | Y 343
 |  | Max Net Quantity Per Package | 2 L
Passenger & Cargo Aircraft | Packing Instruction |  | 355
 | Max Net Quantity Per Package |  | 60 L
Cargo Aircraft Only | Packing Instruction |  | 366
 | Max Net Quantity Per Package |  | 220 L
Actual Net Quantity in Package | 5 L

## Slide 40: Non Radioactive
Correct Package
UN 2841
Di-n-amylamine
SHIPPER
ABC Chemicals
1 Chun Wan Road
Chek Lap Kok
Hong Kong
CONSIGNEE
XYZ Pty LTD
3 Airport Road
Singapore
4G / Z30 / S / 22 GB / 667788
Front:
Left:
Right:
CATHAY PACIFIC
AWB No.
160 8800 8782
Destination Total No. of Pcs
SIN 1
Fast Cargo HK Ltd.
HAWB No. Origin
HKG-1234 HKG
Destination HAWB Pieces
SIN 1

## Slide 41: Non Radioactive
Incorrect Package
UN 2841
Di-n-amylamine
SHIPPER
ABC Chemicals
1 Chun Wan Road
Chek Lap Kok
Hong Kong
CONSIGNEE
XYZ Pty LTD
3 Airport Road
Singapore
4D / Z30 / S / 22 GB / 667788
Front:
Left:
Right:
CATHAY PACIFIC
AWB No.
160 8800 8782
Destination Total No. of Pcs
SIN 1
Fast Cargo HK Ltd.
HAWB No. Origin
HKG-1234 HKG
Destination HAWB Pieces
SIN 1

## Slide 42: Non Radioactive
Correct DGD
ABC Chemicals
1 Chun Wan Road
Chek Lap Kok
Hong Kong
HONG KONG
160-88008782
1 1
XYZ Pty LTD
3 Airport Road
Singapore
SINGAPORE
XXXXX
XXXXXXXX
UN
2841
Di-n-amylamine
3 (6.1) III
1 Fibreboard x
5 L
355
24 Hour emergency contact: 852-27471111
Ming Lee
01 AUG 2024
Ming

## Slide 43: Non Radioactive
Incorrect DGD
ABC Chemicals
1 Chun Wan Road
Chek Lap Kok
Hong Kong
HONG KONG
160-88008782
1 1
XYZ Pty LTD
3 Airport Road
Singapore
SINGAPORE
XXXXX
XXXXXXXX
UN
2841
Di-n-amylamine
3 III
1 Fibreboard x
5 L
355
24 Hour emergency contact: 852-27471111
Ming Lee
01 AUG 2024
Ming

## Slide 44: Non Radioactive
Correct Air Waybill
Chemicals
Dangerous Goods as per associated DGD

## Slide 45: Non Radioactive
Incorrect Air Waybill
Chemicals
Dangerous Goods as per DGD

## Slide 46: Non-Radioactive (UN 3480 Sec. IB)

## Slide 47: Non Radioactive (UN 3480 Sec. IB)
Shipment Information
Actual Net Quantity in Package | 8 kg
UN Number |  | UN 3480
Proper Shipping Name |  | Lithium Ion Batteries
Class |  | 9
Packing Group |  | /
Packing Instruction |  | 965 – Section IB
Passenger aircraft | Net Quantity of Lithium Ion Cells or Batteries Per Package | Forbidden
Cargo aircraft | Net Quantity of Lithium Ion Cells or Batteries Per Package | 10 kg

## Slide 48: Non Radioactive (UN 3480 Sec. IB)
Correct Package
UN 3480
Lithium ion batteries
SHIPPER
ABC Chemicals
1 Chun Wan Road
Chek Lap Kok
Hong Kong
CONSIGNEE
XYZ Pty LTD
3 Airport Road
Singapore
Front:
Left:
Right:
CATHAY PACIFIC
AWB No.
160 8800 8782
Destination Total No. of Pcs
SIN 1
Fast Cargo HK Ltd.
HAWB No. Origin
HKG-1234 HKG
Destination HAWB Pieces
SIN 1
UN3480

## Slide 49: Non Radioactive (UN 3480 Sec. IB)
Incorrect Package
UN 3480
Lithium ion batteries
SHIPPER
ABC Chemicals
1 Chun Wan Road
Chek Lap Kok
Hong Kong
CONSIGNEE
XYZ Pty LTD
3 Airport Road
Singapore
Front:
Left:
Right:
CATHAY PACIFIC
AWB No.
160 8800 8782
Destination Total No. of Pcs
SIN 1
Fast Cargo HK Ltd.
HAWB No. Origin
HKG-1234 HKG
Destination HAWB Pieces
SIN 1
UN3480

## Slide 50: Non Radioactive (UN 3480 Sec. IB)
Correct DGD
ABC Chemicals
1 Chun Wan Road
Chek Lap Kok
Hong Kong
HONG KONG
160-88008782
1 1
XYZ Pty LTD
3 Airport Road
Singapore
SINGAPORE
XXXXX
XXXXXXXX
UN
3480
Lithium ion batteries
9
1 Fibreboard x
8 kg
965 IB
24 Hour emergency contact: 852-27471111
Ming Lee
01 AUG 2024
Ming

## Slide 51: Non Radioactive (UN 3480 Sec. IB)
Incorrect DGD
ABC Chemicals
1 Chun Wan Road
Chek Lap Kok
Hong Kong
HONG KONG
160-88008782
1 1
XYZ Pty LTD
3 Airport Road
Singapore
SINGAPORE
XXXXX
XXXXXXXX
UN
3480
Lithium ion batteries
9
1 Fibreboard x
8 kg
965
24 Hour emergency contact: 852-27471111
Ming Lee
01 AUG 2024
Ming

## Slide 52: Non Radioactive (UN 3480 Sec. IB)
Correct Air Waybill
Lithium ion batteries
Dangerous Goods as per associated Shipper’s Declaration – CAO

## Slide 53: Non Radioactive (UN 3480 Sec. IB)
Incorrect Air Waybill
Lithium ion batteries in compliance with Section IB of PI 965
Dangerous Goods as per associated Shipper’s Declaration – CAO

## Slide 54: Radioactive (Type A Package)

## Slide 55: Radioactive (Type A Package)
Shipment Information
Radionuclide in Package | Lu-177, Special Form
Activity | 9.2 GBq
Transport Index | 0
Category | I-White
Gross Weight | 12 kg
Dimension | 38 x 22 x 32 cm
UN Number | UN 3332
Proper Shipping Name | Radioactive material, Type A package, Special Form
Class | 7

## Slide 56: Radioactive (Type A Package)
Correct Package
UN 3332
Radioactive material,
Type A package,
Special Form
Shipper
XYZ Hospital
200 Front Street E
Toronto, Ontario
Canada M5J 2L7
Lu-177
9.2 GBq
Consignee
ABC Research Ltd.
12 Wan Po Road
Tseung Kwan O
Hong Kong
TYPE A
F
RadMed Co
Front:
Lu-177
9.2 GBq
Back:
CATHAY PACIFIC
AWB No.
160 8800 8782
Destination Total No. of Pcs
HKG 1
Air Cargo Express
HAWB No. Origin
YYZ-1234 YYZ
Destination HAWB Pieces
HKG 1
Right and Left:

## Slide 57: Radioactive (Type A Package)
Incorrect Package
UN 3332
Radioactive material,
Type A package,
Special Form
Shipper
XYZ Hospital
200 Front Street E
Toronto, Ontario
Canada M5J 2L7
Lu-177
9.2 GBq
Consignee
ABC Research Ltd.
12 Wan Po Road
Tseung Kwan O
Hong Kong
TYPE A
F
RadMed Co
Front:
Back:
CATHAY PACIFIC
AWB No.
160 8800 8782
Destination Total No. of Pcs
HKG 1
Air Cargo Express
HAWB No. Origin
YYZ-1234 YYZ
Destination HAWB Pieces
HKG 1
Right and Left:

## Slide 58: Radioactive (Type A Package)
Correct DGD
ABC Research Ltd.
12 Wan Po Road
Tseung Kwan O
Hong Kong
TORONTO
160-88008782
1 1
XYZ Hospital
200 Front Street E
Toronto, Ontario
Canada M5J 2L7
HONG KONG
XXXXX
XXXXXXXX
UN
3332
Radioactive material, Type A package,
Special Form
7
Lu-177
1 Type A Package x
9.2 GBq
I-
White
24 Hour emergency contact: +1 905-600-0000
Tom Green
01 AUG 2024
Tom
Special Form Certificate
CA/123/S
Attached

## Slide 59: Radioactive (Type A Package)
Incorrect DGD
ABC Research Ltd.
12 Wan Po Road
Tseung Kwan O
Hong Kong
TORONTO
160-88008782
1 1
XYZ Hospital
200 Front Street E
Toronto, Ontario
Canada M5J 2L7
HONG KONG
XXXXX
XXXXXXXX
UN
3332
Radioactive material, Type A package,
Special Form
7
Lu-177
1 Type A Package x
9.2 GBq
I-
White
24 Hour emergency contact: +1 905-600-0000
Tom Green
01 AUG 2024
Tom

## Slide 60: Radioactive (Type A Package)
Correct Air Waybill
Radioactive material
Dangerous Goods as per associated Shipper’s Declaration

## Slide 61: Radioactive (Type A Package)
Incorrect Air Waybill
Radioactive material
Dangerous Goods as per associated Declaration

## Slide 62: Case 4B – Radioactive (Type B(U) Package)

## Slide 63: Radioactive (Type B(U) Package)
Shipment Information
Radionuclide in Package | I-123, solid
Activity | 7.4 MBq
Transport Index | 0.2
Category | III-Yellow
Gross Weight | 55 kg
Dimension | 50 x 50 x 55 cm
UN Number | UN 2916
Proper Shipping Name | Radioactive material, Type B(U) package
Class | 7

## Slide 64: Radioactive (Type B(U) Package)
Correct Package (cylinder)
UN 2916
Radioactive material, Type B(U) Package
Consignee
MMM Hospital
1 Soi Phetchaburi
Bangkok 10310
Thailand
Shipper
ABC Research Ltd.
100 Harbor Blvd
Los Angeles CA
92626 USA
TYPE B(U)
US/24/BU
S/N#001
I-123
7.4 MBq
0.2
Permissible Gross Weight 55 kg
Front:
Back:
I-123
7.4 MBq
0.2

## Slide 65: Radioactive (Type B(U) Package)
Incorrect Package (cylinder)
UN 2916
Radioactive material, Type B(U) Package
Consignee
MMM Hospital
1 Soi Phetchaburi
Bangkok 10310
Thailand
Shipper
ABC Research Ltd.
100 Harbor Blvd
Los Angeles CA
92626 USA
TYPE B(U)
US/24/BU
S/N#001
I-123
7.4 MBq
0.2
Front:
Back:
I-123
7.4 MBq
0.2

## Slide 66: Radioactive (Type B(U) Package)
Correct DGD
MMM Hospital
1 Soi Phetchaburi
Bangkok 10310
Thailand
LOS ANGELES
160-88008782
1 1
ABC Research Ltd.
100 Harbor Blvd
Los Angeles CA
92626 USA
BANGKOK
XXXXX
XXXXXXXX
UN
2916
Radioactive material, Type B(U) package
7
I-123
Solid
1 Type B(U) Package x
7.4 MBq
II-
Yellow
T.I.
0.2
DIM:
50x
50x
55 cm
24 Hour emergency contact: +1 310-400-4000
Tom Green
01 AUG 2024
Tom
Type B(U) Package Certificate
US/24/BU
Attached

## Slide 67: Radioactive (Type B(U) Package)
Incorrect DGD
MMM Hospital
1 Soi Phetchaburi
Bangkok 10310
Thailand
LOS ANGELES
160-88008782
1 1
ABC Research Ltd.
100 Harbor Blvd
Los Angeles CA
92626 USA
BANGKOK
XXXXX
XXXXXXXX
UN
2916
Radioactive material, Type B(U) package
7
I-123
1 Type B(U) Package x
7.4 MBq
II-
Yellow
T.I.
0.2
DIM:
50x
50x
55 cm
24 Hour emergency contact: +1 310-400-4000
Tom Green
01 AUG 2024
Tom
Type B(U) Package Certificate
US/24/BU
Attached

## Slide 68: Radioactive (Type B(U) Package)
Correct Air Waybill
Radioactive material
Dangerous Goods as per associated DGD – CAO

## Slide 69: Radioactive (Type B(U) Package)
Incorrect Air Waybill
Radioactive material
Dangerous Goods as per associated DGD